## Slide 1: Block Diagram PWM Case
DAC
Crossbar
Subtractor
Ramp Generator
Comparator
TDC

## Slide 2: 2 parts- 1) functional aspect, 2) parameters – energy, delay etc
Voltage level – Vdd – default =1.8V
Weights – precision – number of bits
DAC precision – number of bits
  T period for 1 pulse
Crossbar output – parameters
Slope of Ramp Generator
TDC number of bits output
TDC time precision – least time it can measure
  Coarse and fine

## Slide 3: DAC
T period of 1 pulse
Number of bits it can handle

## Slide 4: Crossbar
Functional aspect:
OF – On off ratio – parameter
Ron – parameter
C - parameter
Xi – inputs we take
Have black box to add parameters like energy, latency etc.

## Slide 5: Subtractor
Black box which does subtraction operation for 2 columns.
Have scope to add values like energy, latency, etc.

## Slide 6: Ramp Generator
Y=mx function
M is a parameter
Enable the ramp generator
X refers to time steps
Take 0.01 ns as time step
Take default slope as 0.01V/ns

## Slide 7: Comparator
Compare both input values and based on that give a high signal (Stop signal goes high) when ramp starts to be more than Vref – given by subtractor

## Slide 8: TDC
2 inputs – “Start” signal high when ramp generator is initialized
“Stop” goes high when comparator gives output
Subtracted value
Based on the time between these 2 signals- gives output based on output resolution(number of bits to represent output)
E.g. if output is 4 bits – measures

## Slide 9: DAC
ENERGY – no of bits
Delay – pulse period

## Slide 10: crossbar
ENERGY – larger the array size ,resistance and capacitance ,no of bits
Delay – time taken to execute the no of parallel operations based on the selected rows.

## Slide 11: Ramp generator
ENERGY – faster the ramp more power.
Delay – time consumed to meet the crossing point

## Slide 12: Subtractor
ENERGY – to compute the column values based on the array size
Delay – time consumed to perform its operation

## Slide 13: TDC
ENERGY – num_bits taken to represent the output
Delay – time consumed to calculate the digital output based on the start and stop time.